## Slide 1: Human Presence and Activity Detection from WiFi CSI Data using CNN
Md Touhiduzzaman
Samah Ahmad
Maher Al Islam

## Slide 2: Outline
WiFi Sensing
Problem Statement
Dataset
Our Approach
Results
Future Scopes
Conclusion

## Slide 3: 1. WiFi Sensing
What?
  A combination of Wi-Fi and RADAR sensing technology
  Use of the same Wi-Fi transceiver hardware and RF spectrum
  Physical layer in RADAR systems
  Well-defined MAC layer for WiFi sensing
  More Complex Algorithms than in RADAR like FFT, OFDM processing etc.
  Both Communication and Gesture Detection
  Biometric measurements (e.g. breathing[1][2])
[1] https://wballiance.com/resource/wi-fi-sensing/
[2] Wi-Fi Sensing: Revolutionizing Motion Sensing with Wi-Fi technology. Semiconductor Components Industries LLC. July 2020.
Notes: - fine tuned to detect so subtle changes in the environment like breathing
- that shows the depth of the capability of WiFi sensing

## Slide 4: 1. WiFi Sensing
Examples[3]
Controlling Slideshow
Controlling TV From Anywhere
Smart Home Applications
[3] http://wisee.cs.washington.edu/
Notes: * WiSee - Uni. of Washington
* 1st - a person is controlling a slideshow using his wrist movement
* middle - a TV remote alternative is shown using WiFi sensing
* 3rd example - we can turn the lights of the whole apartment on or off using WiFi sensing & smart home appliances as well

## Slide 5: 1. WiFi Sensing
Why?
  More Privacy Safety
  Ubiquitous Gestures than Line of Sight for Cameras
  Less Data Volume to Store in Comparison to Video/Image Data
  Cheaper & Available Hardware
  Whole Body Gestures
  Larger Combination of Events
Notes: Why would someone use WiFi Sensing whereas we have easy to use libraries like OpenCV and other gesture recog. Systems?
- example: Monitoring a patient in a hospital bed
– doing good or in trouble
- huge data volume 24/7
- so costly &
- more computation time to process & learn
- if our patient falls inside the washroom, we cannot monitor there by the camera
* If use WiFi sensing :
- so ubiquitous, no need of being in the Line of Sight
- textual CSI/RSS data
– can ensure privacy more &
- Combination of Events using broader area

## Slide 6: 2. Problem Statement
ai = ?
  where, ai ∈ A = {a1, a2, a3, ..., a12} in an environment ei ∈ E = {e1, e2, e3} by a person si ∈ S = {s1, s2, s3, ..., s30} within a set of classes of actions C = {c1, c2, c3, c4, c5}

## Slide 7: 3. Dataset
Intel 5300 NIC as Access Point (AP)
3 Raspberry Pi connected with each AP as clients
AP with 3 Antennas
30 sub-carrier per NIC per antenna
Total Subcarriers = 3*30 = 90

## Slide 8: 3. Dataset

## Slide 9: 3. Dataset & Preprocessing

## Slide 10: 4. Our Approach

## Slide 11: 4. Our Approach
Variables:
  Batch Size = {100, 256, 512, 1024, 1536, 2048}
  Filter Size = {3x3, 5x5}
  Pool Size = {2x2, 4x4}
  #Filters = {5, 10, 15, 32, 64}
Constants:
  Number of Layers:
    2 Convolution
    1 ReShape
    1 Dense
  Padding=0, Stride=1
  Filter Numbers in latter layers:
    2nd Layer = Twice of the 1st layer
    3rd Layer = Reshaped same size as the 2nd layer
  #Output of the 4th Layer = 12 * 256
  #Output of the 4th Layer = 12

## Slide 12: 5. Results

## Slide 13: 5. Results
* Batch Size is found to be the most significant variable , because this is a well-timed dataset and batch-size can be related to the duration of actions as:

## Slide 14: 6. Future Scopes
Variation of Layer Configurations
Variation of Activation Functions other than ReLU
More Variation of Filter & Pool Size
Application of Denoising Filters like DWT, Hampel, Butterworth, etc.
In the Same Dataset –
  Predict the Class of the Action
  Predict the Person doing the Action
Apply the Model to Other Available Datasets
  Random actions may be challenging, as this dataset is a well-timed one.

## Slide 15: 7. Conclusion
Accuracy 73.3% at best
  Alazrai et. al.[31] achieves 69.78% accuracy with all the 12 actions of the same dataset
  Alsaify et. al. [32] achieves 94% accuracy with just 6 actions from this dataset
Well-Timed Dataset, so Batch-Size is Important
Novelty in Application of CNN for such a varying dataset

## Slide 16: Thank You!
Questions?
Notes: - challenge: Reading the data file into memory - crashing program